## Slide 1: Axle Weights
P&O Ferrymasters
Driver Training Programme 2019 v1

## Slide 2: Axle Weights - Issues
Overweight on the Tractor Unit Drive Axle
Overweight on the Trailer axle
The driver is responsible for the positioning of the load and
ensuring they are not overweight on their drive or trailer axle
The Customer also has a legal responsibility to assist the driver as far as reasonably practicable
Notes: Axle weight infringements come in 2 forms. Tractor Unit drive axles and trailer axles. Although the loader places the load on the trailer. The driver has responsibility for the positioning of the load and ensuring that he is not overweight.

## Slide 3: Axle Weights
8 ton
8 ton
8 ton
Notes: Trailers commonly used on the European traffic are allowed to have 8 ton on each of the trailer axle.
An additional complication and consideration is the difference axle weight requirement for 2 and 3 axle tractor units. Although in the UK you may not have to worry about axle weights with 3 axle units, when on the continent, the trailer will always be collected by a 2 axle tractor unit, and the positioning of the load to comply with axle weights is key
When positioning loads the following generic guidance can be followed.

## Slide 4: Axle Weights – Full Length Loads – 24 ton
Trailer’s Roof supports
12m
Centre of Gravity
Notes: The centre of gravity of a trailer and thus the middles positioning of a load should be just in front of the first trailer axle. When positioning 12m length of uniform load, then the middle of this load should be where the centre of gravity of the trailer

## Slide 5: Axle Weights – Part Length Loads – 24 ton
Trailer’s Roof supports
9m
Centre of Gravity
Notes: 9m length of load should similarly be placed in the middle of the trailer, balanced around the centre of gravity

## Slide 6: Axle Weights – Part Length Loads – 24 ton
Trailer’s Roof supports
7m
Centre of Gravity
Notes: 7m length of load should similarly be placed in the middle of the trailer, balanced around the centre of gravity

## Slide 7: Axle Weights – Part Length Loads – 24 ton
Trailer’s Roof supports
6m
Centre of Gravity
Notes: 6m length of load should similarly be placed in the middle of the trailer, balanced around the centre of gravity

## Slide 8: Axle Weights – Mixed Length Loads – 24 ton
Trailer’s Roof supports
6m
9m
7m
12m
Centre of Gravity
Notes: A combination of lengths of loads need to be loaded around the centre of gravity

## Slide 9: Axle Weights – Single Coil Loads – 24 ton
Trailer’s Roof supports
Centre of Gravity
Notes: In terms of steel coil. Single heavy coils should be positioned around the centre of the trailer, which is normally the second position back in the coil well

## Slide 10: Axle Weights – Multiple Coil Loads – 24 ton
Trailer’s Roof supports
Centre of Gravity
Notes: Multiple coils should be positioned around the centre of gravity, but spread along the coil well, in line with the stanchion positions

## Slide 11: Axle Weights – Signs of overloading
Load not spread over the back axle
Road marks
Flat spots on the tyres
Vehicle struggling to pull away (having to use crawler gears)
Notes: There are some obvious signs of overloading of axle weights. If your vehicle is overloaded on the drive axle then the load will not be spread over the back axles of the trailer. There may be marks on the road or flat spots on the tyres. The tractor unit will be noticeably more difficult to pull away

## Slide 12: Axle Weights – Summary
Trailer’s Roof supports
6m
9m
7m
12m
Centre of Gravity
Notes: Summary of load positioning and axle weights