## Slide 1
UK and European Laws
UK
Road Vehicles (Construction and Use) Regulations 1986
Road Traffic Act 1988 Regulation 40A
Health & Safety at Work act 1974
NETHERLANDS
Ministerie van Verkeer en Waterstaat: Wegenvekeerswet 1994
GERMAN
Straßenverkehrs-Ordnung (StVO): 2009
All Authorities agree that everyone involved in the Transport Chain has a shared responsibility to ensure that the goods are correctly positioned and secured
Receiving
Driving
Carrying
Loading
Consigning

## Slide 2
Enforcement in the UK
HSE view steel loads as the highest risk on the highways.
Enforcement in UK, NL and other EU countries has historically been weak – but not anymore!

## Slide 3
Enforcement in Europe
German police have specialists trained in Load Restraint, and have guidelines that they follow e.g. expect to see anti-slip matting used.
Different regions may have slightly different interpretations of requirements.
Chain of responsibility moving back down the line from the driver to the loader and consigner.
Dienst Vekeerspolitie
Unit MTC

## Slide 4
Load Restraint – Key guidance documents
Note that UK law does not specifically reference any of the guidance documents, but … the enforcing agencies do!
EN 12195-1:2010
EU
DfT Code of Practice
1st Edition 1972; 3rd Edition 2002
UK
VDI: 2700 – 2011
Germany

## Slide 5
Load Restraint Standards – Forces under EN12195
0.8g forward
0.5g backwards
0.5g sliding
0.6g toppling

## Slide 6
Load Restraint – against forward forces – G Force
  80% of the weight forwards
    Under heavy braking the forces are equal to about 60%
    Collision with a light vehicle will raise this to 80%
80% of the weight forwards (0.8 g)

## Slide 7
Forces in European EN12195 - Road
0.8g forward
0.5g back
0.5g sliding
0.6g toppling
1.0g vertically
EN 12195-1:2010
toppling

## Slide 8
Forces in European EN12195 - By Sea
0.3g forward
0.3g back
0.7g sliding
0.7g toppling
1.0g vertically
EN 12195-1:2010
0.3g vertically
B

## Slide 9
Forces in European EN12195 - Intermodal
1.0g forward
1.0g back
0.5g sliding
0.5g toppling
1.0g vertically
EN 12195-1:2010
0.6g toppling

## Slide 10
Load Restraint Methods
Tie-Down Lashing
Containing
Blocking
Direct Lashing
Relies upon friction
Can use a combination to form a SYSTEM
Direct Restraint

## Slide 11
Load Restraint Methods